## Slide 1: MREN Certification Authority
Lidija MIlosavljević
lidija@ac.me
Center of Information Systems
University of Montenegro
Podgorica

## Slide 2: Montenegrin Research and Education Network – MREN
Established in June 2005 as a part of Ministry of Education and Science
MREN is the name given to the collection of all networking services and facilities, which support the communication and information requirements of the education and research community in Montenegro.
Aims to create, promote, offer, participate in and preserve the requisite bases for effective use of modern telecommunication technologies in the education and research in Montenegro.
Main mission : is to connect MREN to GEANT- multi-gigabit pan-European data communications network, reserved specifically for research and education use, via fiber optic with high speed.
Support the substantial use of the Pan-European and world research networks by Montenegrin researchers, scientists, lecturers and students, as well as to facilitate the integration of Montenegrin educational, research and cultural resources in the international information space.
Web site : www.mren.ac.me

## Slide 3: MREN organization
Organizational board (distinguished figures from the Montenegrin academic, governmental and IT sector)
MREN technical management and monitoring
  Center of Information Systems
    University of Montenegro
    Podgorica
    Web site : www.cis.ac.me
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: MREN goals
Coordinate further development of Montenegrin infrastructure and services in academic and high education environments
Include new academic and high educations institutions in MREN
MREN is a member of TERENA and national contact point for projects related with academic network
Coordinate human resources involved with GRID
Organize seminars and training events to help develop and use MREN infrastructure
Create a national GRID development policy
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Montengero GRID initiative - MGI
    MREN coordinates Montengero GRID initiative (MGI)
    MGI members :
      University of Montenegro
      Center of Information Systems
      Faculty of Electrical Engineering
      Faculty of Mechanical Engineering
      Faculty of Metallurgy and Technology
      Faculty of Natural Sciences and Mathematics
      Faculty of Civil Engineering
      Institute of Biotechnology
      T-com (Telecom provider)
      Cikom ltd, Podgorica (ICT company)
      IT Advanced Services ltd. (ITAS), Podgorica (ICT company)
      Hydrological and Meteorological Service of Montenegro
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: MREN involvement
SEEREN-2 (FP6)
SEE-GRID-2 (FP6)
SEE-GRID-SCI (FP7)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: MREN CA
Used CP/CSP Documents:
AEGIS CP/CSP
MARGI CP/CPS
SEEGRID CA CP/CPS
SRCE CA CP/CPS
ArmeSFo CA CP/CPS
Object Identifier (OID): 1.3.6.1.4.1.29544.1.1.1.0
Date: October 2007
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: MREN CA
Naming
C=ME, O=MREN, CN=MREN-CA
C=ME, O=MREN, OU=XXX, CN=Subject-name
[C] Country = ME
[O] Organization = MREN
[OU] Organization Unit = Name of the institution
[CN] Common Name = Name and surname of the person for the personal certificate, DNS name for host or service certificate
(In the last case the DNS FQDN may be prefixed by the value 'host' or the service name separated with a '/' from the DNS FQDN).
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: MREN CA
Certificate Extensions in case of CA root certificate are following:
X509v3 Basic Constraints: critical, CA:TRUE
X509v3 Key Usage: critical, Certificate Sign, CRL Sign
X509v3 Subject Key Identifier: <CA key ID>
X509v3 Authority Key Identifier: keyid: <CA key ID>
X509v3 Issuer Alternative Name: email: mren-ca@ac.me
X509v3 Subject Alternative Name: email: mren-ca@ac.me.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: MREN CA
The values of extensions in case of user certificates are following:
X509v3 Basic Constraints: critical, CA:FALSE
X509v3 Key Usage: critical, Digital Signature, Key Encipherment, Data Encipherment, Key Agreement
X509v3 Extended Key Usage: TLS Web Client Authentication, E-mail Protection
X509v3 Subject Key Identifier: <subject key ID>
X509v3 Authority Key Identifier:
Keyid: <CA key ID>
X509v3 Subject Alternative Name: email:<user's email address>
X509v3 Issuer Alternative Name: email: mren-ca@ac.me
X509v3 Certificates Policies: Policy: <OID of the effective CP/CPS>
X509v3 CRL Distribution Points.

## Slide 11: MREN CA
The values of extensions in case of host and service certificates are following:
X509v3 Basic Constraints: critical CA,FALSE
X509v3 Key Usage: critical Digital Signature, Key Encipherment, Data Encipherment, Key Agreement
X509v3 Extended Key Usage: TLS Web Server Authentication, TLS Web Client Authentication
X509v3 Subject Key Identifier: <subject key ID>
X509v3 Authority Key Identifier:
keyid: <CA key ID>
X509v3 Issuer Alternative Name: email: mren-ca@ac.me
X509v3 Subject Alternative Name: DNS:FDQN
X509v3 Certificates Policies: Policy: <OID of the effective CP/CPS>
X509v3 CRL Distribution Points.

## Slide 12: MREN CA
Certificate
1024 bit or 2048 bit encryption
1 year plus 1 month.
Initial identity validation
Personal certificate
Subject must contact RA or CA in person
id-card, passport or driving license (valid document from official organizations from our country).
Server/Service certificate
The host must have a valid DNS name
The administrator must already possess a valid personal MREN Certificate
The administrator must provide a proof of his or her relation to the host itself.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: MREN CA
Certificate revocation list (CRL)
Max/Min lifetime of the CRL: 30/7
issued at least 7 days before expiration
new CRL will be publish within 1 working day after revocation process
Circumstances for revocation
The CA is informed that the Subscriber has ceased to be a member of or associated with a MREN program or activity
The subscriber’s private key is lost or suspected to be compromised;
The information in the Subscriber’s certificate is wrong or inaccurate, or suspected to be wrong or inaccurate;
The subscriber violates his/her obligations.
The subscriber does not need the certificate any more.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Identification and Authentication for Revocation Request
For persons who do not have a valid MREN certificate, but hold an evidence of a revocation circumstance: by personal authentication as initial identity validation
By signing a revocation request e-mail via a valid personal key corresponding to the certificate that is requested to be revoked which must be a valid, non-expired and non-revoked MREN Certificate.
If the revocation request is for a host or service certificate, then the e-mail must be signed by the private key corresponding to the certificate of the person responsible of the host or service. When e-mail is not an option, the request will be authenticated using the procedure as initial identity validation.
Revocation request by the RA should be done by e-mail, signed with valid RA operator key.

## Slide 15: MREN CA
Types of records archived
The following data and files are recorded and archived by the CA:
certification requests
issued certificates
requests for revocation
issued CRLs
all e-mail messages of correspondence between RA and CA
Each RA must keep log of the following:
for each approved request, how it was approved
for each rejected request, why it was rejected
for each approved revocation request, the reason for revocation
for each rejected revocation request, the reason for revocation and the reason the request was rejected.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Contact details:
Center of Information Systems University of Montenegro
bul. Džordža Vašingtona
81000 Podgorica
Montenegro
Phone: +382 20 242 777
Phone: +382 20 244 406
Fax: +382 20 244 406
E-mail: mren-ca@ac.me
Lidija MIlosavljević
e-mail: lidija@ac.me
Notes: <number>
<footer>
<header>
<date/time>