## Slide 1: Authorization WG Update
David Kelsey
EU Grid PMA, Dublin 19 Jan 2010

## Slide 2: Mandate
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>
EUGridPMA Working Group on Policy Management for Grid Authorisation
  Mandate and aims
To prepare recommendations on policy and global trust issues related to Grid Authorisation (AuthZ)
The initial list of issues will include:
  Minimum requirements and best practice for the operation of a Grid AuthZ attribute authority
  Etc etc etc

## Slide 3: Progress since Jan 2009
Very little!
But, would now be useful to establish best practice as we move into the EGI era
So…To kick-start the activity
I propose to go through some of the issues
See https://grid.ie/eugridpma/wiki/AA_Profile
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 4: AA key
The AA signing key must have a minimum length of 2048 bits and should be dedicated to attribute signing functions and tied to the AASP
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 5: Key protection
Software-based private keys of the AA must be suitably protected by the operating system and must only be accessible by the service, trained personnel with procedural controls.
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 6: Key protection (2)
AAs are encouraged to consider using an HSM which must adopt a similar or better level of security.
Copies of the private key must be encrypted or must only be available in clear-text in a system which is at least as well protected as the original system.
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 7: Key protection (3)
Under “Site Security”
CA profile said...
The pass phrase of the encrypted private key must be kept also on an offline medium, separated from the encrypted keys and guarded in a safe place where only the authorized personnel of the Authority have access. Alternatively, another documented procedure that is equally secure may be used.
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 8: Assertion revocation
There is no revocation.... But RFC3281 has provision for a CRL.
The entire PKC certification path must be verified. Revocation of the AA certificate will kill all assertions signed by the AA. The AC is bound to a specific serial number of the end entity. Revocation of the end entity certificate must stop the issue of ACs. Also RP checks the validity of the identity certificate.
Revoking a specific AC makes no sense as there are many other issued ACs containing the same attributes.
There is no case for revoking ACs.
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 9: Assertion lifetime
Maximum lifetime of the assertion should be 24 hours... expand
Because there is no revocation mechanism.
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 10: Definition of “attribute”
An attribute is a string, a named property which may be associated with an entity... expand this definition
An attribute assertion is a statement that a subject is a holder of a specific attribute.
For VOMS, an attribute is a group, role or generalised attribute.
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 11: Attributes (2)
Explain Relying party requirements on lifetime of attributes, schema etc.
The attribute assertion must link the attribute to one and only one explicitly named entity.
The lifetime of the assertion should take into account the dynamic nature. Not more than 24 hours. (MS)
Dynamic updating of the attribute schema by the VO is required ...why?
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 12: APS
Every AA must have an Attribute Practice Statement (APS Document) and assign it a globally unique object identifier (OID).
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 13: APS (2)
This should at least contain:
  persistent contact details for the AASP
  document their operational environment
  state compliance with this policy
  maintain accurate VO contact information for all the AAs they host and a link to the VO AUP
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 14: APS (3)
This APS should be public and made available, except for the operational environment which must be disclosed to the accrediting body.
APS document should be structured as defined in a template
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 15: AASP naming
The registered name is needed to ensure that different accreditation bodies do not accredit different AASPs with the same name inside the realm of one CA
AASP accrediting body should act as registrar for repository of AASPs
Naming ... AA:<reasonable representation of name of aasp > - <arbitrary non-null string identify the server or VO set by CA or requested by AASP>
Example cern - wlcg-voms
Or cern - voms411.cern.ch
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 16: Accreditation process
Should be one AASP per organisation.
Person requesting should be appropriately authorised by the organisation.
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 17: Accreditation (2)
These guidelines are intended to facilitate accreditation of Attribute Authority Service Providers rather than an individual Attribute Authority (a hardware/software installation) or Virtual Organization (a collaborative organisation). An Attribute Authority Service Provider is an organization (or group within an organization) that runs Attribute Authority Services, including one or more Attribute Authorities, for one or more Virtual Organizations. To achieve sustainability, an AASP should operate AA services as a long-term commitment.
A VO should have an AA operated by a single AASP. If the AA service is replicated for reasons of performance and/or fault tolerance then there must be means of ensuring consistency. If a VO wishes to have a distributed AA operated by multiple AASPs then these AASPs must be accredited individually.
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>

## Slide 18: Accreditation (3)
The AA service should be operated in accordance with the requirements of the VO Membership Management Policy (ref) and this document.
Which body does the accreditation?
  Scaling problems!
19 Jan 10
AuthZ, EU Grid PMA, Kelsey
<number>